## Slide 1: RFID Card Reader
The SPI interface

## Slide 2: Serial Peripheral Interface
Dedicated line for each direction of communication

## Slide 3: Multiple slaves
There are different configurations for multiple slaves
We’re only using one slave

## Slide 4: Configuring the Pi
sudo raspi-config
Interfaces -> Enable SPI
reboot the Pi

## Slide 5: What is RFID?
Radio Frequency IDentification
https://youtu.be/gEQJxNDSKAE
No battery, wireless communication

## Slide 6: Wiring the RC522 -> Pi
3.3V -> 3v3
GND -> GND
MISO -> SPIMISO
MOSI -> SPIMOSI
SCK -> SPISCLK
SDA -> SPICE0
python3 readrfid.py

## Slide 7: Messing around with RFID
Python3 writeToRFID.py
python3 display_rfid_data.py
  Connect LCD screen to I2C to see display
  Recall VCC -> 3.3V, SDA and SCL to their equivalents

## Slide 8: Uses of RFID
Where have you seen it?
Where could it be used?

## Slide 9: Multifactor Authentication
Something you know
  passwords, pins, security questions
Something you have
  RFID card, cell-phone app
Something you are
  Fingerprint scanner, face scan
Somewhere you are
  Geofence, IP address

## Slide 10: Problems with RFID
Speed (typically 40kbps)
Security
Privacy

## Slide 11: Access Cards
Connect LEDs (with resistors)
Red to GPIO 21
Yellow to GPIO 20
Green to GPIO 16
Enter RFID numbers as separate lines in validcards.txt
python3 access_card.py

## Slide 12: Investigation
How can you tell if someone has been attempting to gain access?